## Slide 1: Disassemble Incline strengthen round tube steps
Step 1~Step 4

## Slide 2: Step 1. Please remove pedal on both sides and front/rear end cap 請移除左右踏板以及前後調整盒

## Slide 3: Step 2. Adjust incline to 15 levels and cut the power 升起揚升至15段並斷電

## Slide 4: Step 3. Loose Incline strengthen round tube screw (no.248) near the wheel on left and right side 鬆開揚升補強桿螺絲(左右邊皆須鬆開)

## Slide 5: Step 4. Remove Incline strengthen round tube as following picture 移除揚升補強桿(建議兩側要撐開比較好拿)

## Slide 6: Assemble timing belt steps
Step 1~Step 12

## Slide 7: Step 1. Prepare your timing belt and check where is line mark as picture on right hand side 確認準備好的時規皮帶的記號位置

## Slide 8: Step 2(video). Lift up the front frame to put timing belt 抬起車架前方將時規皮帶放入 P.S move mouse to picture and the play icon will show up

## Slide 9: Step 3(video). Lift up the back frame to put timing belt 抬起車架前方將時規皮帶放入 P.S move your mouse to picture and the play icon will show up

## Slide 10: Step 4. Make sure to align the mark for both side 確認記號位置兩邊相互對齊

## Slide 11: Step 5. Put the hole of timing belt in the middle groove that between rear roller gear and gear 將時規皮帶之打孔處置於後滾筒齒與齒的中間凹槽

## Slide 12: Step 6. Put in front roller and fasten the screw until front roller position is parallel with screw(look down from above) 放入前滾筒並將螺絲鎖緊，前滾筒位置約與螺絲平行處(正上方視角)

## Slide 13: Step 7. double check the mark of timing belt is aligned for both side 再次確認記號位置對齊

## Slide 14: Step 8. Stick 93. BAM9000-250-30 rubber pad from the hole on timing belt. Please use same method to stick it, put them gently do not try to extend it. 貼上泡棉，請由時規上的孔處開始張貼，兩邊時規皆需保持相同的張貼狀況。張貼泡棉時，雙手以自然方式放置泡棉(參考手勢)，勿拉伸泡棉

## Slide 15: Step 9-1. Align to the hole then stick the rubber pad continuously (4 rubber pads on each timing belt) 以切齊孔位方式連續張貼泡棉(一邊時規需要四條泡棉)

## Slide 16: Step 9-2. We highly recommend rubber pad seam can exactly on half of the hole, this will be good look and not easily drop off. 建議泡棉接縫處剛好在孔位的一半，較美觀跟不易脫落

## Slide 17: Step10(video). Put the 313. P-5123 Pedal gasket on rubber pedal 放置尼龍墊片 P.S move your mouse to picture and the play icon will show up

## Slide 18: Step 11. Check the direction of peal (note: It’s look down from above angle. If need to lock the screw, kindly rotate pedal together) 確認跑帶方向(請注意 此為上方視角方向，若旋轉至下方要組螺絲時也需一併選轉跑帶)

## Slide 19: Step12(video). Put on no.95 pad plate and lock 96. nylon nut 放上鐵片，並繫上螺帽 P.S move your mouse to picture and the play icon will show up

## Slide 20: Recover everything same as how you disassemble at the beginning